## Slide 1: Silicon Photonic Accelerated Memory Pooling For Efficient Compute Resource Allocation
Zhenguo Wu and Keren Bergman
zw2542@columbia.edu
Lightwave Research Laboratory
Columbia University, New York, NY
Aug 20th, 2025

## Slide 2: Memory Challenges in Scaling Large Language Models
GPU Memory Limitations
The growth rate of high-bandwidth memory (HBM) per GPU is much slower than the rapid scaling of Large Language Models (LLMs).
The growing gap limits batch size scaling and adds distributed training/inference complexity.
H100 OPs:Bytes
Memory Bound
Compute Bound
Training
Inference
Arithmetic Intensity Variations
LLM models exhibit diverse arithmetic intensities across workloads for training and inference, as well as between the prefill and decode stages of inference.
Each workload (or stage) imposes unique demands on compute power and memory bandwidth.
Gap

## Slide 3: Current Compute & Memory Pooling Architecture
HBMs are placed around the periphery of the compute die using short-reach electrical I/Os.
  HBM’s wide I/O and high pin count requires short electrical traces, restricting it to areas near the compute die.
  Compute die's periphery length restricts the number of HBMs that can be integrated locally.
  Limited memory capacity scaling.
Memory Pooling: compute pool connects to memory pool via a high-speed electrical interconnect.
Local HBMs serve as high-bandwidth memory suppliers (lower capacity).
Remote memory units (e.g., DDR, GDDR) act as capacity expanders via an electrically interconnected fabric.
SOTA GPU
HBM
HBM
HBM
HBM
HBM
HBM
Electrical I/O
PCIe
SoTA Compute Architecture
Compute Pool
Electrical Interconnect
Mem
Mem
Mem
Mem
Mem
Mem
Mem
Mem
Memory Pool
GPU
GPU
GPU
GPU
Current Memory Pooling Architecture

## Slide 4: Enabling Silicon Photonic Technologies
Custom Designed Transceiver PIC [1]
Co-Packaged/Embedded Photonic I/Os
[1] Wang, Yuyang, et al. “Co-designed silicon photonics chip i/o for energy-efficient petascale connectivity.” IEEE Transactions on Components, Packaging and Manufacturing Technology. IEEE, 2024
[2] Dai, Liang Yuan, et al. "Ultra-scalable microring-based architecture for spatial-and-wavelength selective switching." 2023 IEEE Silicon Photonics Conference (SiPhotonics). IEEE, 2023.
In3
Out1
Out2
Out3
In2
In1
Optical Circuit Switches
Custom Designed Switch PIC [2]
1. Massively parallel bandwidth
2. Distance-independent scaling
Modulated Signals
Data
Data
Data
Comb
Laser
Micro-ring resonator (MRR)
Embedded Photonic Transceiver
Total = 16 Tbps

## Slide 5: Expanding the Memory Pooling Design Space
SOTA GPU
HBM
HBM
HBM
HBM
HBM
HBM
Electrical I/O
PCIe
SiP I/O Embedded GPU
HBM
HBM
HBM
HBM
HBM
HBM
SiP I/O
PCIe
Fully Disaggregated GPU
(Total ~ 30 TBps = 240 Tbps)
PCIe
SiP I/O
SiP I/O
SiP I/O
﻿Conceptual Embedded SiP Chip I/O
Designed and fabricated transceiver PIC
Semi-Disaggregated GPU
HBM
HBM
SiP I/O
SiP I/O
PCIe
HBM
Total = 2 TBps
Compute die’s shoreline width is used a critical resource.
Unified high-bandwidth domain for memory and network communication
(16 Tbps)

## Slide 6: SiPAM: Silicon Photonic Accelerated Memory-Pooling
SiP I/Os: 3D integrated EIC and PIC through flip-chip bonding
  Each SiP I/O : 16 links × 32 / link × 32 Gbps / = 2 TBps
Number of integratable I/Os:
  = Available compute die shoreline width
  = Edge width per SiP I/O
Fully Disaggregated
Compute Unit
PCIe
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
EIC
PIC
Frequency
Comb Driven I/Os
16 x 32λ x 32 Gbps
= 2 TBps / IO
EIC
PIC
~8 mm
shoreline
16 links
…
…
…
HBM
HBM
EIC
PIC
HBM
HBM
EIC
PIC
HBM
HBM
HBM
HBM
…
HBM
HBM
HBM
HBM
Memory Pool
EIC
PIC
EIC
PIC
EIC
PIC
SiPAM Compute Architecture
EIC-PIC 3D Integration
Flip-chip
PIC
EIC
(De-)Interleaver Control
Compute/Mem Interface
32-Channel Tx Link 0
32-Channel Rx Link 1
…
(De-) Interleaver
(De-) Interleaver
…
…
Fiber Array
32-Channel Rx Link 0
32-Channel Tx Link 1
32-Channel Tx Link 0
32-Channel Rx Link 1
32-Channel Rx Link 0
32-Channel Tx Link 1
b)
Memory Pool: Optically Connected Multi-Stack HBM [3]
Multiple HBMs connect to a single SiP I/O chiplet
Number of integratable MUs / IO:
  = SiP I/O bandwidth
  = MU bandwidth
[3] Ou, Y., Zhang, H., Rovinski, A., Wentzlaff, D., & Batten, C. (2025). Optically Connected Multi-Stack HBM Modules for Large Language Model Training and Inference. IEEE Computer Architecture Letters.

## Slide 7: SiPAM: Silicon Photonic Accelerated Memory-Pooling
[4] Michelogiannakis, George, et al. "Efficient intra-rack resource disaggregation for HPC using co-packaged DWDM photonics." 2023 IEEE International Conference on Cluster Computing (CLUSTER). IEEE, 2023.
[5] Cho, A., Saxena, A., Qureshi, M., & Daglis, A. (2024, November). COAXIAL: A CXL-centric memory system for scalable servers. In SC24.
MU
MU
MU
Memory Tray
CU
OCS
OCS
OCS
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
WSS
OCS
OCS
OCS
OCS
OCS
OCS
OCS
OCS
MU
MU
Memory Interface
OCS
OCS
OCS
Compute Trays
SiPAM Network Topology
d)
Compute Tray
Compute Tray
Compute Tray
Memory Tray
Memory Tray
Compute Tray
Optical Switches
Optical Switches
SiPAM Rack
Optical Interconnect
Each SiP I/O can be flexibly allocated for high-speed memory access or network communication.
One-shot reconfiguration per workload.
SiPAC’s physical design: replaces electrical packet switches (EPS) with optical circuit switches (OCS) in a BCube topology
  Intra-rack resource disaggregation model [4] for a bounded increase in memory latency.
  CXL is a promising memory semantic interconnect technology:
  Increased memory latency can be mitigated by increasing CXL bandwidth when the memory system is fully loaded [5].

## Slide 8: Optimization Methodology
Goal: Determine the optimal configuration for compute power, memory bandwidth, and capacity for each workload.
  Compute Intensity (CI): # of required FLOPs per byte of data loaded to keep cores active.
  Hardware
  Arithmetic Intensity (AI): # of actual FLOPs performed for each byte of data loaded.
  Workload
Roofline Model
Compute Bound
Memory Bound
Peak FLOPs/s
Memory Bandwidth
System Performance
(reconfigurable)
Design CI = AI
CI

## Slide 9: Optimization Methodology
Peak Compute FLOPs
(1)
FLOPs/s
Workload Arithmetic Intensity
(2)
FLOPs/s
I FLOPs/Byte
Required Memory Bandwidth
(3)
FLOPs/s
I FLOPs/Byte
Number of memory units to satisfy memory bandwidth requirement
MU
MU
MU
MU
MU
MU
MU
(4)
MU
MU
MU
Mem BW:
PCIe
Distribution of SiP I/Os for memory and network communication
(5)
SiP I/O for memory
SiP I/O for network
Number of CUs + parallelisms
(6)
Goal: Determine the optimal configuration for compute power, memory bandwidth, capacity for each workload.

## Slide 10
[6] Isaev, Mikhail, et al. "Calculon: a methodology and tool for high-level co-design of systems and large language models." SC 2023.
Megatron-126M
Anthropic-52B
GPT3-175B
Megatron-1T
Arithmetic Intensity: profiled using Calculon
Capacity Requirement: profiled using Calculon
Baseline Configuration:
  NVLink (scale-up) + InfiniBand (scale-out)
SiPAM Configuration:
  SiPAC network
  Optimized # GPUs, memory capacity and bandwidth
Workload & Configurations
Evaluation Setup – Calculon [6]
SiPAM Configuration:
MU
MU
MU
Memory Tray
CU
OCS
OCS
OCS
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
OCS
OCS
OCS
OCS
OCS
OCS
OCS
OCS
MU
MU
Memory Interface
OCS
OCS
OCS
Compute Trays
Baseline Configuration:
NIC: up to 800 Gbps / GPU
NVL Domain: up to 72 GPUs
InfiniBand / Ethernet Network
NIC
GPU
GPU
NIC
NVSwitch
NIC
GPU
GPU
NIC
NVSwitch
NIC
GPU
GPU
NIC
NVSwitch

## Slide 11
Hardware – Nvidia GPU Based
Single CU | FP16 TFLOPs | Mem Cap (GB) | Mem BW (TBps)
Nvidia A100 | 312 | 40 | 1.5
Nvidia H100 | 1000 | 80 | 3
Nvidia B100 | 3500 | 192 | 8
SiPAM* | 3500 | Up to 720 | Up to 30
* Assuming B100 as CU and HBM3E as MU
Cluster of 1024 CUs | FP16 PFLOPs | Mem Cap (TB) | Mem BW (PBps)
Nvidia A100 | 320 | 41 | 1.5
Nvidia H100 | 1024 | 82 | 3.1
Nvidia B100 | 3584 | 197 | 8.2
SiPAM* | 3584 | Up to 737 | Up to 31
Cluster Size: up to 1024 GPUs
SiPAM Configuration:
MU
MU
MU
Memory Tray
CU
OCS
OCS
OCS
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
CU
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
SS
OCS
OCS
OCS
OCS
OCS
OCS
OCS
OCS
MU
MU
Memory Interface
OCS
OCS
OCS
Compute Trays
Baseline Configuration:
NIC: up to 800 Gbps / GPU
NVL Domain: up to 72 GPUs
InfiniBand / Ethernet Network
NIC
GPU
GPU
NIC
NVSwitch
NIC
GPU
GPU
NIC
NVSwitch
NIC
GPU
GPU
NIC
NVSwitch
Evaluation Setup – Calculon [6]

## Slide 12: Simulation Results - Training
Workloads: Megatron-126M/5B/22B/40B/1T, Anthropic 52B, Chichilla-64B, GPT3-175B (Training)
Baseline: Up to 256 B100 GPUs each with fixed 192 GB HBM memory @ 8 TBps total memory bandwidth
SiPAM: Up to 256 GPUs, with compute, memory bandwidth, and capacity optimized based on each workload
SiPAM tracks arithmetic intensity closely, while the baseline remains constant
SiPAM improves training time by up to 3.5x
Lower is Better

## Slide 13: Simulation Results - Inference
SiPAM tracks arithmetic intensity closely, while the baseline remains constant
SiPAM improves inference time by up to 3.5x
Lower is Better
Workloads: Megatron-126M/5B/22B/40B/1T, Anthropic 52B, Chichilla-64B, GPT3-175B (Inference)
Baseline: Up to 64 B100 GPUs each with fixed 192 GB HBM memory @ 8 TBps total memory bandwidth
SiPAM: Up to 64 GPUs, with compute, memory bandwidth, and capacity optimized based on each workload

## Slide 14: Performance Under Limited Compute Resource
Configurations:
  Workload: GPT3-175B and Megatron-1T
  Red cells: no feasible parallelization strategy
  Darker color: higher iteration time
Takeaway: SiPAM consistently enables feasible deployment of larger models under constrained GPU resources
  SiPAM flexibly allocates memory capacity and bandwidth.
  For a fixed GPU-HBM combination, iteration time decreases as the number of available GPUs increases.
  For a fixed number of GPU, newer GPU generations yield lower iteration time.

## Slide 15: Compute & Memory Technology Scaling
A100
H100
B100
Inference
A100
H100
B100
Training
Configurations:
  Workload: GPT3-175B
  Network size: 128 GPUs
Cross GPU-HBM pairing
Takeaway: SiPAM consistently outperforms the baseline by allocating the needed compute and memory resources
  Newer GPU generations outperform earlier ones.
  For each GPU generation, performance improves as memory generation advances.

## Slide 16: System Efficiency Analysis
H100 (HBM2E)
A100 (HBM2)
Relative Performance
Relative Performance
Relative Performance
B100 (HBM3E)
2.52
Configurations:
  Workload: Megatron-1T
  Metrics: System Efficiency & Iteration Time (inset shows relative performance)
SiPAM consistently outperforms the baseline in both efficiency and iteration time.
System Efficiency =

## Slide 17: SiP I/O Bandwidth Scaling
Megatron-1B
Training
Megatron-1B
Inference
Megatron-1T
Inference
Megatron-1T
Training
Configurations:
  Workload: Megatron-1T & Megatron-1T
  Per I/O Bandwidth: 512 Gbps to 16 Tbps
  Total injection bandwidth / GPU:
    A100/H100: 6 Tbps to 192 Tbps
    B100: 7.6 Tbps to 240 Tbps
Takeaway: Newer GPU generations with higher compute capability require greater memory bandwidth to achieve continued performance scaling.
A100 on Megatron-1B: performance plateaus
  Compute throughput becomes saturated

## Slide 18: Conclusion
Problems addressed: memory capacity & bandwidth bottlenecks in AI/ML
Design:
  Direct photonic integration along the perimeter of the compute die
  Unified high-bandwidth communication domain
Optimization: co-designed roofline-model based allocation algorithm
Results:
  Showed up to 3.5x faster iteration time
  Highlights the critical need for bandwidth scaling in next-generation compute.
Future Works:
  Cost and power modeling
  Capture network demand in addition to memory demand

## Slide 19: Acknowledgement
19